## Slide 1: Lithium-Ion Battery Response Training
Battery Basics and Hazards

## Slide 2: Battery Basics and Hazards
Unit 2
Notes: Unit 2 Battery Basics
The calibration step to ensure everyone is speaking the same language.

## Slide 3: Battery Fires are on the Rise
Notes: Incidents are on the rise for at least two reasons.
Energy density of batteries has risen over the past 12 years and will presumably continue to rise.
At the same time production of batteries, and thereby batteries out in the world has increased and is projected to increase another 5x-10x over the next 5 years.
This will lead to more transport incidents and more disposal/accumulation of batteries as they reach their end of life.

## Slide 4: Exponential Increase - Infrastructure
Federal Infrastructure Investment and Jobs Act (11/15/2021)
  $6 Billion - Battery Storage
  $7.5 Billion - Rapid charging stations – 500,000 along highways and in communities
  $1 Billion - School Buses
Notes: Why are we talking about this now?
Basic statistics. We have a massive increase in the presence of these batteries due to government subsidies. Their price point has decreased and is accessible by more of the population.

## Slide 5: Number of Incidents Globally
https://www.ul.com/insights/lithium-ion-battery-incident-reporting
Notes: Why are we talking about this?

## Slide 6: Total Incidents by Category
https://www.ul.com/insights/lithium-ion-battery-incident-reporting
Notes: Why are we talking about this?

## Slide 7: Battery Types (Primary)
Non-rechargeable Batteries (Alkaline)
Stable, no significant energetic releases.
Consistent energy, long-term power, but loses strength over time.
Long shelf life.
Non-rechargeable Batteries (Lithium Metal)
Stable, large energy density.
Can provide strong energy surges even after a period of low discharge
Lithium metal found inside is extremely water reactive
Notes: Alkaline batteries are stable and discharge consistently over their life time but loses strength over time and will lose the ability to power some devices before they are fully drained. No energetic releases, no lithium or other reactive metals.
Lithium Metal batteries contain the largest stored energy potential, not rechargeable, contain lithium metal which is water reactive.
Let’s look inside these

## Slide 8: Battery Types (Secondary)
Lead Acid Batteries
Stable, low energy density
Contains lead and sulfuric acid
Risk of explosion due to oxygen and hydrogen generation during charging
Nickel Cadmium (NiCad)/Nickel Metal Hydride (NiMH) Batteries
Rechargeable and stable
Suffers from “memory effect”
Can be smothered (METAL-X, sand, etc.)
Water application can cause hydrogen gas release
Notes: Lead Acid batteries are low energy and stable. They are low cost and make up a large percentage of batteries utilized and are a large waste management concern due to presence of lead.
NiCad and NiMH are difficult to damage. Can take deep discharges. They may suffer from the “memory effect”. Fires should be smothered as water application can cause hydrogen production. Water can be used in ventilated areas for extinguishment.

## Slide 9: Lithium-Ion Battery Types
18650
18 x 65 mm
2170
21 x 70 mm
Prismatic
Cell
Pouch
Cell
Cylindrical cells (18650) are the most common cell in mobility devices (bikes, scooters, etc.) and are used by electric vehicles with 3,000 to 7,000 cells
Prismatic and Pouch Cells are found in industrial and consumer electronics, respectively; both are used in electric and hybrid vehicles
Notes: The 18650 cylindrical cell is 3/4 inches in diameter and 2.5 inches long and is the most common battery in mobility devices such as E-Bikes, Electric Scooter, Hovercrafts, drones, etc. Electric vehicles can use thousands of cylindrical cells in series to form the vehicles battery
Prismatic Cells are found in some hybrid vehicles. Pouch Cells are often found in laptops and cellphones.
All these variations of batteries come with Pros and Cons from more or less stable, more or less compartmentalization, more or less resistant to physical damages. However, for the purpose of our AWARENESS training, they all behave very similarly during an emergency.

## Slide 11: Lithium-Ion Battery (LIB) Construction

## Slide 12: Cylindrical vs Prismatic

## Slide 13: Electrical Definitions
Watt (W): Represents power at a given moment.
Watt-hour (Wh): Represents the total energy used over a specific time period.
Example: A 100-watt light bulb turned on for one hour would use 100 watt-hours of energy.
Notes: A "watt" measures the rate of energy usage at a specific moment, like how fast electricity is flowing, while a "watt-hour" measures the total amount of energy used over a period of time, essentially combining power (watts) with time to calculate the total energy consumed; think of it like speed vs distance, where watts are like speed and watt-hours are like the total distance traveled

## Slide 14: Battery Configurations
The most common configuration for Electric Vehicle (EV) batteries is a series-parallel hybrid.
Series Connection: Increases the battery pack’s voltage, which is vital for providing the necessary power to drive the vehicle.
Parallel Connection: Increases the battery pack’s capacity, essential for storing the energy required to achieve the desired range.
To calculate the gross battery pack size, multiply the total parallel capacity in ampere-hours (Ah) by the battery pack's nominal voltage in volts (V). The result is in watt-hours (Wh).
Notes: Battery configuration refers to the arrangement of individual battery cells within the battery pack often utilizing modules. This configuration affects the voltage, capacity, power output, and overall performance.
The most common configuration for Electric Vehicle (EV) batteries is a series-parallel hybrid. In this setup, multiple cells are connected in series to increase the battery pack's voltage, and multiple groups of series-connected cells are then connected in parallel to increase the battery pack's overall capacity.

## Slide 15: LIB Chemistries
Acronym | Name | Formula
LCO | Lithium Cobalt Oxide | LiCoO2
NCA | Lithium Nickel Cobalt Aluminum Oxide | LiNiCoAlO2
NMC | Lithium Nickel Manganese Cobalt Oxide | LiNiMnCoO2
LMO | Lithium Manganese Oxide | LiMn2O4
LFP | Lithium Iron Phosphate | LiFePO4
LTO | Lithium Titanate | Li2TiO3
Chemistries cannot always be mixed in recycling
Energy Density by Chemistry
Notes: LCO, NCA, NMC and LMO can be combined in the recycling process
LFP (Lithium Iron Phosphate) requires separation prior to shredding and recycling, it is the least valuable.
LTO (Lithium Titanate) also requires separation but is rare and more valuable than other chemistries

## Slide 16
Notes: Incident in China

## Slide 19: LIB Toxic/Flammable Vapors
Image Source: Larsson et. al, 2017.
Flammable and Toxic Vapors:
Hydrogen (30%-50%)
Carbon Monoxide
Carbon Dioxide
Hydrogen Fluoride
Hydrogen Chloride
Hydrogen Cyanide
Phosphoryl Fluoride
Organic Solvent Droplets
Ethane, methane, and other hydrocarbons
Notes: Source: Toxic fluoride gas emissions from lithium-ion battery fires. Larsson F, Andersson P, Blomqvist P, Mellander BE. Sci Rep. 2017 Aug 30;7(1):10018. doi: 10.1038/s41598-017-09784-z. Erratum in: Sci Rep. 2018 Mar 22;8(1):5265. PMID: 28855553; PMCID: PMC5577247.

## Slide 20: Differences in LIB Fires
Toxic gas release → hazardous atmosphere
Hydrogen gas release → explosion potential
Higher than normal burn temperatures → thermal runaway reaction
Chemical reaction – rapid degradation
Does not require external oxygen
Nearly impossible to stop once it starts
Could happen in seconds or days
Re-ignition is possible – minutes, hours, days, weeks, months, even years later!
Notes: - What makes these fires different?
- Very Toxic, they Burn hotter, they don't need oxygen, they produce explosive gases, caused by a Thermal Runaway reaction which cannot be stopped and creates a domino effect on neighboring batteries. This can lead to re-kindle many days or even weeks later, even after fire and batteries appear "C

## Slide 21: Causes of Battery Failure
Notes: Batteries can fail for a few primary reasons: mechanical, electrical, and thermal. Mechanical includes manufacturing defects and dendrite formations as well as physical damages.
Each one of these failures can lead to battery degradation and thermal runaway

## Slide 22: Dendrites

## Slide 23: Propagation
  Propagation results in domino effect
    Thermal Runaway heat in one battery will trigger Thermal Runaway in neighboring cells
  Limiting propagation is primary goal
    Cooling neighboring cells may prevent propagation
    Removing exposed cells (i.e., removing other e-bikes, loose cells, etc.)
Notes: What is propagation? The domino effect of fire from one battery to the next inside a battery pack

## Slide 24: Preventing Battery Failure
A battery pack built together with a battery management system with an external communication data bus is a smart battery pack.
A smart battery pack must be charged by a smart battery charger.
Notes: A Battery Management System (BMS) is an electronic component of the battery and can be considered as the brain of the system that manages the charge and discharge processes of a pack. The primary job of a BMS is to protect the battery (by preventing operation of any cell outside its safe operating area).
Even a smart battery will not work properly without a smart battery charger! This is why using non-OEM equipment causes so many problems

## Slide 25: Primary Presentations of LIBs
Energy Storage Systems
Electric Vehicles
Micro-mobility
Consumer Products
Notes: Lithium-Ion Battery systems can be broken down into 3 major categories: Energy Storage Systems or BESS, Electric Vehicles Including Hybrid (HEV), Plug in Hybrid (PHEV), hydrogen fuel cell (CH2) or purely electric (BEV), and Micro Mobility Devices
Here you can see that, at the end of the day, the battery packs are essentially the same. In a vertical configuration it is an BESS, horizontally it is a BEV and the individual packs power the micro mobility.