## Slide 1: Battery De-energizing Exercise

## Slide 2: Hands-On De-energizing Exercise
Overview of the Exercise
  Each team will de-energize 2 batteries
  Each team will make their own unique brine solution (typically 0.5 to 15% salt) in a solo cup – Use only 1 salt for your solution
  Once the solution is made, place the cup inside the paint can as secondary containment
  Voltage measurements will be collected several times, starting with an initial measurement now
  Plan how you will recover the batteries from the cup for subsequent measurements
H&S Considerations
  Purposely damaging batteries
  Gas generation during deenergizing
  Secondary containment considerations
  In case of an emergency

## Slide 3: Hands-On Deenergizing Exercise
Supplies:
A cup with plain water
2 batteries
A voltmeter
Access to various salts
Access to a scale
Procedure:
Record the starting voltage of your batteries
Determine how you will place and remove batteries from the cup
Record your salt solution