## Slide 1: Lithium-Ion Battery Response Training
Transportation, Packaging and Shipment of Batteries

## Slide 2: 49 CFR 173.185 Lithium Cells and Batteries
Presents regulations for shipment of batteries
  173.185(f) – presents regulations for shipment of Damaged, Defective, or Recalled (DDR) Batteries
  Shipper identifies DDR status

## Slide 3: DOT Restrictions for DDR Batteries

## Slide 4: Identification of DDR Batteries
Determined by the generator

## Slide 5: DOT Involvement at Sites
DOT has been involved for several purposes
  Investigation of where the bad batteries came from
  Following up with EPA’s procedure to make sure EPA is shipping appropriately
Lesson Learned: Involve DOT early and often
Example: DOT Involvement at Batteries and Electronics Recycling Inc. (BERI, Mount Horeb)
  May 11, 2020: Initial by EPA OSC to discuss the site
  July 22, 2020: Follow-up contact by EPA OSC that raised red flags
  July 24, 2020: First site visit
  July 28, 2020: Second site visit
  August 06, 2020: Third site visit
  August 25, 2020: DOT Special Permit application submitted
  September 09, 2020: Last site visit
  October 16, 2020: DOT Special Permit issued

## Slide 6: Transportation Options for DDR Batteries
Fully Regulated
Emergency Waiver
Outside of Commerce
Special Permit

## Slide 7: Fully Regulated
Can be onerous and expensive. May be prohibitive depending on scale.
1 battery per outer container, regardless of size of the outer container or size of the battery
Battery must go in an inner container (typically a plastic bag)
Bag must be cushioned by something that is soft, absorbent, non-combustible, and non-conductive
Following Lakes Parkway, DOT issued a safety notice that, while allowed by regulation, plastic is not advised for outer container material.

## Slide 8: Emergency Waiver
Typically issued during Stafford Act responses
Must be held in each vehicle
Allows for transport from source to the staging area, within 50 miles of source area
Transportation after staging must be in compliance with HMR

## Slide 9: Outside of Commerce
Not typically performed, but was discussed with DOT for SoCal Wildfires
49 CFR 171.1(d) - Functions not subject to the requirements of the HMR
(5) Transportation of a hazardous material in a motor vehicle, aircraft, or vessel operated by a Federal, state, or local government employee solely for noncommercial Federal, state, or local government purposes.
If a government employee drives a government vehicle they are generally considered not “in commerce”
If a government contractor is driving, or if the vehicle is not a wholly government owned vehicle, the transportation would be considered “in commerce”.

## Slide 10: DOT Special Permits
Companies may request a special permit that describes an approach
EPA Regions may request a special permit specific to a site
Manufacturers may sell products with a special permit already approved that describes how to use their product
Allow for operations outside of the Hazardous Materials Regulations, providing a similar level of security can be met
Require a submittal for approval and can take 7-90 days to be approved

## Slide 11: DOT SP-16532: held by ER, not site-specific
Special Permit to package multiple “small” lithium ion batteries
  Up to 400 lbs in a standard 55-gallon drum

## Slide 12: DOT SP-21329: held by R4, site-specific
Special Permit to package multiple “large” lithium ion batteries (>300Wh, 14 lbs)
  Up to 180 lbs in a Call2Recycle drum ($800 per drum)

## Slide 13: Manufacturer Special Permits
Each product will have specific limitations for watt hours, both per battery and total capacity, and packing instructions